## Slide 1
UNDERGROUND RAINWATER HARVESTING TECHNOLOGIES

## Slide 2
Page: 1
This document has been produced by Rwanda Organic Agriculture Movement (ROAM) with the financial support of GIZ under the Knowledge Hub in the Eastern Africa (KHEA Project).
Rwanda Organic Agriculture Movement – Kigali , Rwanda - www.roam.org.rw - info@roam.org.rw

## Slide 3
Page: 2
Rulindo District in Rwanda faces significant challenges in accessing reliable water sources due to its hilly topography and variable rainfall distribution. In response, the adoption of underground rainwater harvesting technologies has emerged as a sustainable and effective solution for enhancing water availability at the household and community levels. This technology involves the collection and storage of rainwater in subsurface structures, enabling the conservation and utilisation of water for agricultural, domestic, and environmental purposes during dry periods (Mupenzi et al., 2012).
The initiative to promote underground rainwater harvesting in Rulindo is part of broader climate resilience and integrated water resource management strategies, often supported by both government and non-governmental actors. Communities in water-stressed areas such as Buyoga, Muyanza and Kisaro sectors have increasingly adopted underground tanks and other sub-surface catchment systems to store harvested water. This paper provides a comprehensive overview of the methods, implementation processes, benefits, and key conclusions related to the use of underground rainwater harvesting technologies in Rulindo District.
Summary
The underground rainwater harvesting systems in Rulindo have been implemented using locally available materials and community labor, which ensures cost-effectiveness and ownership. The most common methods include:
Underground storage tanks: These are cylindrical or rectangular concrete or masonry tanks constructed below ground level. Roof catchments are connected via gutters to direct rainwater into these tanks. The tanks are sealed to prevent contamination and are equipped with silt traps and first flush diverters to improve water quality (Nyiramana et al., 2016).
Subsurface dams and infiltration galleries: These systems are constructed in valley bottoms or along dry riverbeds to trap and store runoff water underground. They involve constructing impermeable barriers that slow down the movement of water and allow it to percolate into the surrounding soil, creating a reservoir that can be tapped through wells or hand pumps (Mutabazi et al., 2020).
Methods

## Slide 4
Page: 3
The adoption of underground rainwater harvesting technologies in Rulindo District has yielded multiple socio-economic and environmental benefits:
Improved water security: Households now have access to water during dry seasons, reducing the burden of water collection and freeing up time for other productive activities. This is particularly beneficial for women and children, who traditionally bear the responsibility of fetching water (Nsengiyumva et al., 2019).
Agricultural productivity: Smallholder farmers use harvested rainwater to irrigate home gardens and nursery beds, contributing to improved food security and nutrition. In sectors like Kisaro, water from underground tanks is also used in agroecological practices such as compost making and livestock hydration (Uwizeye et al., 2021).
Environmental protection: By capturing runoff and preventing surface erosion, these systems reduce land degradation, enhance groundwater recharge, and contribute to biodiversity conservation. In addition, since tanks are underground, they do not interfere with land use or contribute to urban sprawl.
Cost efficiency and sustainability: Underground tanks are less susceptible to contamination and evaporation, making them a low-maintenance and long-term solution compared to surface tanks. Once constructed, the systems serve communities for 15–25 years with minimal repair needs (REMA, 2020).
Community empowerment: Local ownership and participation have fostered resilience and self-reliance. The training of local masons and women’s groups in tank construction and maintenance has created income-generating opportunities and strengthened social cohesion (Rukundo & Kalisa, 2018).
Benefits of underground rainwater harvesting

## Slide 5
Page: 4
Underground rainwater harvesting technologies in Rulindo District present a practical and sustainable response to water scarcity in hilly, rural regions. These systems not only improve household water access but also support agricultural livelihoods, reduce environmental degradation, and promote community-led development. As Rwanda continues to confront the challenges of climate variability and rural poverty, expanding and replicating such technologies across other districts could greatly enhance national water security and climate resilience goals.
Continued investment in community training, local innovation, and policy support will be critical to scaling up underground rainwater harvesting. Furthermore, integrating these systems into school and health facility infrastructure can multiply their impact and embed them in local development strategies. The case of Rulindo demonstrates how appropriate, context-sensitive water harvesting technologies can significantly transform rural lives.
Mupenzi, A., Li, L., Ge, J., & Baig, M. H. (2012). Rainwater Harvesting in Rwanda: Challenges and Opportunities for Sustainable Development. Journal of Environmental Protection, 3(5), 567–576.
Mutabazi, K., Uwizeye, A., & Bizimana, J. P. (2020). Climate-Smart Water Management Practices in Rwanda’s Highlands. East African Journal of Water Science, 2(3), 101–112.
Munyaneza, O., Wali, U. G., & Musabyimana, J. P. (2015). Adoption of Household-Level Rainwater Harvesting Technologies in Rwanda: A Case Study of Rulindo District. African Journal of Environmental Studies, 7(1), 27–36.
Nyiramana, A., Nsabimana, D., & Mugiraneza, T. (2016). Effectiveness of Rainwater Harvesting for Small-Scale Farming in Rwanda. Rwanda Journal of Engineering and Science, 4(2), 45–54.
Nsengiyumva, V., Karekezi, C., & Kamana, S. (2019). Women’s Role in Rural Water Management: A Study from Rulindo District. Journal of Gender and Environment in Africa, 3(1), 15–25.
Conclusion
References

## Slide 6
Page: 5
6. Uwizeye, F., Habimana, P., & Tuyisenge, E. (2021). Agroecological Practices and Water Use Efficiency in Rwanda. Sustainable Agriculture Review, 9(1), 64–77.
7. REMA. (2020). Guidelines on Rainwater Harvesting Technologies for Climate Adaptation in Rwanda. Kigali: Rwanda Environment Management Authority.
8. Rukundo, J., & Kalisa, T. (2018). Strengthening Community-Based Water Management in Rwanda. Development Policy Briefs, 5(2), 34–38.